## Slide 1: TESP Overview
2/13/19

## Slide 2: Base Learning Steps
Simulating with GridLabD
  Syntax for simulation
  Available inputs and outputs
Python
  Basic python syntax
    Importing modules
    Functions
    Loops
  Using lists and dictionaries efficiently
  Managing .json files with Python

## Slide 3: TESP - Overview
Command line simulation manager
FNCS is the time-step manager
Developers can create ‘TEAgents’ that:
  Run once per time step
  Interface with the simulators
  Process intermediate simulator output
  Control simulator inputs
https://tesp.readthedocs.io/en/latest/TESP_Overview.html

## Slide 4: TESP – Details
Simulators message format:
  “topic/keyword=value”
  Topic: the simulator sending the message
  Keyword: The part of the simulation being sent
Messages are published or subscribed
Each simulator defines its subscriptions with a .yaml file
  Defines simulator name, time delta, and subscribed values
  Set FNCS_CONFIG_FILE = <file_name>.yaml

## Slide 5: Running a Simulation
Start the FNCS Broker
For each simulator
  Set FNCS config file
  Start the simulator
Easiest to do in a batch script
TESP has GUI tools as well
  Have not been explored yet

## Slide 6: Basic TESP Workflow
Build individual simulations – design GridLabD Simulation
Define subscribed values for each simulator
Write a TEAgent to manage simulation
  Run a loop for each FNCS time step
  Read/Process any necessary simulator values
  Write any intermediate metrics to .json files
  Publish new simulator values

## Slide 7: TE30 Example Simulation
30 homes with Solar power in GridLab-D
1 Large School Building in EnergyPlus
1.3 MW Invariant “Base Load”
Feeder simulated with PYPOWER
https://tesp.readthedocs.io/en/latest/SGIP1_Example.html

## Slide 8: TE30 Control/TEAgent
Currently uses the simple auction agent from PNNL
  Grants each house an HVAC load based on the LMP of distributed solar and distribution feeder
Additional Functionality can be added
  Batteries alongside distributed solar
  Switches to control inverter power flow
    Either charge batteries or send to grid
  Switches could be controlled by publishing from the TEAgent
  Max inverter power output (if GridLabD supports)
Do not yet have a modified proof of concept
  Runtime error in simulation

## Slide 9: TE30 Values Available for Subscribe/Publish

## Slide 10: Future Steps
1. Demonstrate TE30 proof of concept
  Time Estimate: <1 week from today
2. Design a GridLabD simulation/find suitable existing example
  Likely will not use PyPower or EnergyPlus in first version
  TESP Support tools
    Automatically generate simulations
  Adequately document simulation parameters
  Time Estimate: <1 week from start

## Slide 11: Future Steps
3. Write a TEAgent that controls the simulation
For each time step in the simulation:
  Report current simulation values to the transactive energy system
  Collect and record cleared transactions from the system
  Publish the cleared transactions when their timestep is reached
  Time Estimate: 1-2 Weeks from start
5. Build interface for the transactive energy system to control TESP
  Time Estimate: ?
6. Develop any tools needed to visualize/analyze simulation results

## Slide 12: Items to Learn
Debug the example simulation, determine source of runtime error
Options available for generation/load control:
  Control consumption by each house
  Switches for inverter/batteries/solar
  Inverter maximum power output